## Slide 1: (Selected) Results from GOCE++ Dynamical Coastal Topography and tide gauge unification using altimetry and GOCE. Summary of findings and progress on GNSS reflectometry for Coastal sea level. Ole B. Andersen, P Knudsen, K. Nielsen, C. Hughes, R. Bingham, G. Woppelmann, M. Gravelle, S. Padillo, L. Fenoglio-Marc, M. Kern + S. Williams (NOC)

## Slide 2: ESA (ITT) Goce + Height System Unification Roadmap (2011-2014):
2015:
ESA issued an
ITT (GOCE ++)
To focus on individual elements and impact of GOCE…
Project
extended until
early 2019
Courtesy: Gruber et al., 2014)

## Slide 4: GNSS Equipped Tide gauges (SONEL)

## Slide 6
Misfit is on the order of 8-9 cm with geoids at the full resolution

## Slide 7: Software Architecture for creating coastal MDT
GOCE++DYCOT Coastal MDT Software Toolbox.
Command line interface written in R.
Allow filtering combining different MSS + GOCE geoids
Allows integration of MDT with TG,
Error estimation.
Available for free download from gocehsu.eu homepage

## Slide 8: Comparison at NW European coast.
Tide gauges Raw satellite MDT, Filtered combined Sat+TG MDT
Misfit between MDT and TG of 6 cm for combined coastal MDT
Comparable for 9 cm mitfit between MDT (ECCO etd) and TG.
Difference dominated by small scale geoid errors/omissions.

## Slide 9
GNSS-R for coastal MDT.
Evaluation vs Sentinel-3 for coastal
sea level observations -
PROMISING BUT PRELIMINARY RESULTS

## Slide 11
Co-located GNSS reflectrometric stations
and Sentinel-3 SAR altimetry (within 10 km)

## Slide 12
Esbjerg – North Sea coast (Denmark)
2.3 km to Sentinel-3B
Data
No S3B data available
Yet.

## Slide 13
Barcelona
2.8 km between Sentinal-3A and GPS tide gauge.

## Slide 14
GNSS (Grey) vs Sentinel 3A (blue)
Work in progress. Still several unaccounted biases.
More to come at AGU/EGU.

## Slide 15: Summary
GOCE ++ DYCOT results are appearing on gocedt.eu and paper is in press
General comparison between global MDT and TG shows 9 cm nois dominated by short wavelength geoid errors.
MDT evaluation with Tide Gauges is promising for ”geodetic approach”, and in general agreement on the 5-7 cm is found.
New extension of the project to investigate GNSS-R for coastal sea level information for possible MDT enhancement. Preliminary evaluation against Sentinel-3A in coastal regions.
More to follow.