## Slide 1: Nye Muligheder med satellite Altimetry
  Ole Baltazar Andersen, DTU Space +
  Carsten, Mai, Henriette, Louise, Adil, Stine, Heidi,
  Rene, Abbas, PerK, Trine, Tim, m. fl.
Nye muligheder:
  Længere tidsserier (næsten 30 år -> klima)
  Øget opløsning (fra 5 km til 5? meter)
  Nye sensorer (Laser)

## Slide 2: Længere tidsserier:
Globalt
Centrale Arktis
Beauford Gyre
Rose and Andersen, 2020
Weng and Andersen, 2019

## Slide 3: Globale relative vandsstands-ændringer
GEUS notat (2017)
Ludwigsen et al., 2020

## Slide 4: GPS + Tidevandsstationer
Fundamentale for at løse global/relative problematik
Vigtig at Tidevandsstationer udstyres med GPS
13 GNSS-R
Candidate sites
(F-B. Madsen)

## Slide 5: Muligheder for at øge opløsning
Kleinherenbrink et al. 2020
Ny processering (SWATH, SarIN multitarget)
Fully Focused C2 SAR to 5 meter.

## Slide 6: Measuring elevation, one photon at a time…
Photon-counting lidar,
launched Sep 2018
3 km
3 km
90 m
Footprint size: 17 m
Flight direction
10.000 pulses per second - corresponds to 0.7 m between pulses at the surface.
Some photons will penetrate water, so we can observe the lake beds of (some) supra-glacial lakes, i.e. lakes on the ice sheet surface. This allows us to estimate lake water volumes.
The ice sheet surface is visible as areas with a high concentration of photons

## Slide 7
Ship soundings
Depths from
satellite imagery
Depth [m]
Depth [m]
Depth [m]
gt1r
gt2r
gt1r
gt2r
gt1r
gt2r
Grønlands bathymetri – Sammenligning med GST multibeam og optisk .

## Slide 8: Creating high-resolution DEMs of the changing ice sheet surface
Data coverage (Cryosat-2 and ICESat-2)
The laser will reflect from the snow surface. ICESat-2 thereby provides dense coverage of unambiguous data for surface elevations.
Creating a DEM for an area around Helheim Glacier in summer 2019:
DEM (1x1km)
High-resolution elevation data along fluxgates at glacier outlets around the ice sheet margin help to constrain the annual mass loss from the Greenland ice sheet

## Slide 9: Og I 2022 kommer SWOT
3 generations
Billeddannende
Nadir altimeter.