## Slide 1: Sea level extreme and projections surges, tides and waves
Ole B. Andersen.
DTU Space, Denmark
2020

## Slide 2: Overview of this week (extremes)
Sea level rise and impact…….
Climate Models and sea level Projections
Sea level rise and sea level extremes:
Article Discussion:
Contributions to sea level extremes:
  Contribution from Ocean Tides
  Contribution from Winds + Waves
  Contribution from Changing currents + Sea level change.
Sea level extremes – observations:
Working with Newlyn – Annual + extreme. (might skip)
Impacts

## Slide 3: Observed Sea level rise EXPLAINED
Global sea level rise explained by
Eustatic (Add)
And Steric (heat)
ξ(t) = Z0(t) + T(t) + S(t) + ΔO(t).

## Slide 4: Climate models and SL projections

## Slide 5
12 Years Sea Level
Change (1993-2004)
12 Years Sea Surface
Temperature change.

## Slide 6: Projections of Sea level. Semi Empirical model could be:
A physical model for sea surface height changes could be tempeture
This holds to good approximation for temperature and sea-level changes during the 20th century, with a proportionality constant of 3.4 millimeters/year per °C.
We use this to go forward in time: -> Semi empirical model
We know that from Greenland melting
600 gTons result in 0.5 mm water.
We could add Antarctica and Continental glacier models from models.
Vupti we have SEMI EMPIRICAL SEA LEVEL PROJECTION.

## Slide 7: Different flavours
Empirical (not even a climate model but just projection).
Semi Empirical (physical scaled by proxy factors).
AO-GCM (atmosphere ocean global climate models - Coupled)
EMIC models (intermediate complexity - Coupled)

## Slide 8: Climate models (Coupled)

## Slide 9: Climate models

## Slide 10: EMIC = Earth-System Models of Intermediate Complexity

## Slide 12: RCP – Representative Concentration pathways.
Radiative forcing values in year 2100 relative to pre-industraial values (+2-6 +4.5 +6 and +8.5 W/m2. RCP 4.5 and RCP 8.5 gives like global mean temperature increase of 2-3.6 or 3.2-5.4 in year 2081-2100. RCP 8.5 is Business as usual.

## Slide 13: IPCC Intergovermental panel of climate change projections. ”Coupled models” Intercomparison phase (CMIPS)
Coupled model includes atmosphere – versus normal ocean model
Also models are run for different RCP forcing.
6 normal Global models used:
  ACCESS1.0 (CSIRO)
  ACCESS1.3 (CSIRO-BOM),
  CSIRO-Mk3.6.0 (CSIRO-QCCCE Australia),
  EC-EARTH (EC-EARTH consortium)
  GFDL-ESM2G, and
  GFDL-ESM2M (NOAA Geophysical Fluid Dynamics Laboratory, USA).
  BUT THERE ARE ALSO OTHER MODELS (NOT SO CONSERVATIVE)

## Slide 14: 2100 Projections
Sea surface temperature
Change will give 15 cm
Sea level rise due to
Steric expansion in upper
2000 meters.

## Slide 15: Sea level projections

## Slide 17: Excersize 1 – Empirical SL projection…
Create your own Sea level projections into 2100
Load TPJ_mean.mat
Time: t_TPJ=(1993+1/24:1/12:2020)‘ -time_now (=2020) <- Shift origin
p_TPJ=polyfit(t_TPJ,TPJ_mean,2);
Projection (first set time into future:
t_future=(1993+1/24:1/12:2100)’-time_now;
Multiply t_future x p_TPJ to get sea level projection
1) linear: B x t_future + C
2) Quadratic A x t_future**2 + B x t_future + C

## Slide 18: Denmark in year 2100 DMI model (notice uncertainty)

## Slide 21: Break.

## Slide 22: Extremes along Europe’s coast.
Article by Vousdoukas et al. AGU journal open access:
Interesting as it is a detailed view of extreme sea level in the future.
Before we discuss – let me introduce usage of nested model…….
E(t) = max(T(t)) + max(S(t)) + max(Δ O(t)) + Z0(t).
Changes in Z0(t) is given as relative SL(model)

## Slide 23: Vousdukas et al. 2017.
Nested models vs Global models

## Slide 26: What is Vousdoukas is trying to say is:
Predicting future extreme sea levels (ESL) has large REGIONAL VARIATION.
Local effects will create local variations in ESL.
Sea level rise if frequently not the largest component

## Slide 27: Sea Level Extremes – Group discusssion / presentation
Group 1: Figure 2 + Figure 3 (findings).
Group 2: Figure 5 (Contribution of weather extremes) + Figure 6
Group 3: Figure 8 + Table 1 (Evolution of a 100 year extreme)
Group 4: Figure 9 + Table 2 (Return period of present day 100 year extreme)

## Slide 29: Tide and Storm Surges Extremes
ξ(t) = Z0(t) + T(t) + S(t) + O(t).
T(t) is a (mathematical) function of the sun and moon.
S(t ) = (”random”) function of Pressure and Wind.
Low atmospheric pressure create high water level.
Wind forces the water to pile up along the coast.

## Slide 30: Standard Deviation of Tides and Other time varying signals

## Slide 31: Tides T(t) are LARGEST AT THE COAST.
Some countries have a profound interest in tidal research.

## Slide 32: Tides are fun:

## Slide 34: Tidal Forces.
Difference (P1-O) is the Tide producing force =
Force =

## Slide 35: Basic Frequencies
The angular speed can be described using a series of predefined frequencies
The I’s are small integer (Doodson numbers).

## Slide 36: Look into the sky and observe……….

## Slide 37: Tidal Pattern - Spring / Neap tides

## Slide 38: “Acqua Alta”

## Slide 39: Projection -> Tides in year 2100 will get smaller

## Slide 40: Queensland sea level during Surge

## Slide 41: Tides and Storm Surges
ξ(t) = Z0(t) + T(t) + S(t) + O(t).
The astronomical tides are modified by the weather to greater or lesser extent.
If severe weather couples with high tides storm surges occur.
S(t ) = function of Pressure and Wind.
Low atmospheric pressure create high water level.
Meteorological effects are greatest in winter.
Let se an example……..

## Slide 42: Storm surges
Storm surges are well known globally.
Storms surges = Hurricanes (USA)
Hurricanes = Cyclones (i.e., Australia)
Cyclones = Typhones (Japan)
My Holiday in Key West
Florida Oct 2017

## Slide 43: storm surges
A deep centre of low pressure
situated over Scandinavia
produces northerly winds
Wind stress forces surface
waters into the “bottle-neck”
of the English Channel
Flow is restricted by the Straits of Dover and sea levels rise along the adjacent coasts of East Anglia and the Netherlands
4. Other key ingredients include high Spring tides and on-shore winds

## Slide 44: Inverted barometer (IB) effect
The inverse response of sea level to changes in atmospheric pressure =>
A static reduction of 1-mb in atmospheric pressure will cause a stationary rise of 1-cm in sea level . Why winter is worse……….
1000mb
980mb
20cm
Lower Atmospheric Pressure
Notes: IB (mm) = 9.948 * ( 1013.3 - P )

## Slide 45: Storm event. Hurricane Florence 10 Sep 2018.

## Slide 46
If it has been calculated based on past hurricane records that a Category 5 hurricane has a return period of 100 years, this essentially means that there is a 1 in 100 chance (1%) that this will occur in any single year.
a return period of 100 years does not mean that we can’t get two ‘100 year hurricanes’ in two or three consecutive years.

## Slide 47: Quantifying storms (easy) Return periods and Events
Return period P = (n+1)/m
n length of record (100 years),
m = number of recorded incidents or events.
A 100 year event is measured once is 100 years
– this has 1 percent change that it MIGHT occur during any year.
Similarlay a 50 year event or a signal with a return period period of 50 years
– this has 2 percent change that it MIGHT occur during any year.

## Slide 48: Quantify Storm Surges is not so easy – its not the same damage .
A list of some of the largest storm surges, and the
Impact on human population. Forecasting and ”knowledge”
Should diminish the loss of lives in the future.

## Slide 49: Derive statistics from tide gauge. Annual maxima (Newlyn 84 years)

## Slide 50: Derive statistics from tide gauge records.
Probability of sea level z being exceeded in a year is P(z).
Probability of no exceedance is (1-P(z))
In Two years the Probability of no exceedance is (1-P(z))2
Risk of reaching level z in such period is then 1-(1-P(z))2
Risk in a period T is then.
Risk = 1-(1-P(z))T
This is frequently used when constructing off-shore structures.
Bridges / wind mills / oil rigs / dikes etc etc.

## Slide 51
If you create a structure for a 100 year event or an event z with a probability of P(z) = 0.01
then the Risk (R) will be 0.62 of encountering this event during the first 100 years.
Similar statistics to rolling a dice and not wanting a 6’er……

## Slide 52: The “best” we can do. Annual Exceedance at Newlyn
Determine the value of P(z) can be done using the annual exceedance probability at a tide gauge like Newlyn because extreme weather event tend to have a preference to happened during winter

## Slide 53
28 times the annual water level exceeded 3 meters.
In 84 years this is one out of 3 years or a return period of 3 years.

## Slide 54: Fairly equal to a Gaussian distribution

## Slide 55: Showing figure in another way. 3 meters has return period of 3 years

## Slide 56: Including sea level rise

## Slide 57: Including 20 cm sea level rise.
A 3 meter was a 30 year event but becomes nearly annual event
3.2 m

## Slide 58: With increasing sea level return period decreases For places with small tides MORE EXTREME. 100 year event for Aabenraa becomes 10 year event with 25 cm sea level rise.

## Slide 59: Fits with Vous

## Slide 60: Stormsurge BODIL
Though sampling is not ”perfect” the Cryosat-2 occational observations are
Extremely valuable for coastal research and safety.
2013 December Storm Surge Bodil/Xavier was captured by Cryosat-2. Caused 2 meter surge (largest on record) in Kattegat and severe flood damage in Denmark. Bodil was a 1000 Year event

## Slide 61: Maybe there is something we dont know Modifying statistics ??????

## Slide 62: Question / discussion (time permitting) :
How can we even talk about an 100 or 1000 year event
It is VERY VERY DIFFICULT.
AND SEA LEVEL IS SLOWLY CHANGING STATISTICS
Best guess is “the larger the event – the more in-frequent it is”
Some kind of extrapolation (qualified guessing) must be used

## Slide 63: Increased waves in future projections……
Under RCP we will encounter greater surges
And we will expect greater significant and actual wave height
The actual water level will/might be increased as the
Surge Level SSL has an added wave component.
Hs is significant wave height (DELFT NL surge model)
E(t) = max(T(t)) + max(S(t)) + ΔO(t) + Z0(t).

## Slide 64: Waves

## Slide 65: Waves …………

## Slide 66: Significant wave height (10% of time this is exceeded by Extreme WH)

## Slide 67: North Sea - Winter vs Summer

## Slide 68: Dramatic Changes ”tipping point” ξ(t) = Z0(t) + T(t) + S(t) + ΔO(t).
Mainly contribution from Z, but also some from O(t)

## Slide 69: Currents might change ΔO (t)???

## Slide 70: Extreme water level
E(t) = max(T(t)) + max(S(t)) + Δ O(t) + Z0(t).
Changes in Z0(t) + Δ O(t) from Models

## Slide 71: Total extreme sea level (incl Tides)

## Slide 72
Are you knowledgeable about
Sea Level Rise?
How much ?
Causes ?
Impacts ?
Increased Flooding is covered.
Other effects:
Notes: http://sealevel.jpl.nasa.gov
http://climate.nasa.gov/SeaLevelViewer/seaLevelViewer.cfm
http://sealevel.colorado.edu/

## Slide 73
Cliff erosion
Source: Tyndall Centre for Climate Change Research
suspect?

## Slide 74: Coastal erosion and accretion
1 cm rise in MSL erodes approx 1m horizontally of beach
SLR has a profound effect on the rate of sedimentation
Varying of sedimentation rates -> changing vegetation zones e.g. growth/shrinkage of marshes (high tide water level regions)
Storm surges force large quantities of shore-face sediments through inlets -> create tidal deltas/barriers
River flow (Florida must pump water)
1m
0.01
Notes: Movement of sediment from tidal region to beneath near-shore waters
Change to rate of sedimentation due to change in weight of overlying water column
Wetlands/salt marshes – high tide water level regions
e.g. mangrove ecosystems: provide natural protection against storm surges/hurricanes;
sedimentary traps: stabilise coastlines;
home to commercially exploited fish
-in danger of being overcome by rising sea-levels (natural rate of mangrove rise:~2/3 mm yr-1)

## Slide 75
R = G(L/H)S
  H = B + h*
  R = shoreline recession due to a sea-level rise S
  h* = depth at the offshore boundary
  B = appropriate land elevation
  L = active profile width between boundaries
  G = inverse of the overfill ratio
Source: Nicholls, 1998
Bruun Rule (One of the processes affecting sandy beaches)
Notes: Assessing erosion involves using the Bruun Rule for straight areas of coastline. The assumption is that the profile conserves its average or equilibrium shape relative to sea level. Using appropriate boundary conditions, the profile shape defines all the information necessary to predict the response to sea level rise. To maintain the profile shape the upper part of the profile erodes and the lower part of the profile accretes, translating the shoreline landward.
Source: Nicholls, 1998.
R = G(L/H)S
  where: H = B + h*
  R = shoreline recession due to a sea-level rise S
  h* = depth at the offshore boundary
  B = appropriate land elevation
  L = active profile width between boundaries
  G = inverse of the overfill ratio

## Slide 76
Vulnerable coastal/island regions

## Slide 77
Mega Coastal Cities:
Populations >8 million
(over 50% of US population (110 million) live in coastal areas
(over 40% in Europe
Highly populated Delta regions -> Migration
http://www.survas.mdx.ac.uk
Vulnerable populated regions

## Slide 78: People close to the coast

## Slide 79: Increased salinity in estuaries
Saltwater will penetrate farther inland and upstream in estuaries (i.e. estuarine salt wedge)
Higher salinity impairs both surface water and groundwater water supply
Saltwater intrusion would also harm ecosystems:
  aquatic plants and animals e.g. salt marshes, mangroves
  Higher salinity has been found to decrease seed germination
  Flooded agricultural land takes a long time to recover
Decline of coastal commercial fisheries
e.g. Salinity intrusion has already been cited as primary reason for reduced oyster harvests in Delaware and Chesapeake Bays in the USA
Notes: Impair:損害,減少,削弱
Germination:發芽,萌芽
Oyster:牡蠣,蠔,沈默者

## Slide 80
Mitigation

## Slide 81: Amager Faelled is at 1 meter below sea level. However Ørestaden is planned for 1 meters sea level rise

## Slide 82: Dikes

## Slide 83: Dikes, Levees and Floodwalls. New Orleans (Katarina, Levee failure)

## Slide 84: Dike protection.

## Slide 85: The Guardian 2020

## Slide 86
Thanks.