Description and comparison between Mean Sea Srfaces in the GOCINA project.

Mean Sea Surfaces (hereafter called MSS) are by-products of satellite altimetry. Referenced to an Earth ellipsoid, they contain the geoid plus the mean dynamic dynamic ocean topography (MDT).

Men sea surfaces are commonly used by geodesists and geophysicists to analyse geoid undulations, and studying crustal deformation, or Earth interior dynamics. Oceanographers using satellite altimetry can reference sea surface heights (hereafter called SSH) to the MSS. Due to the non perfect satellite positioning for repeat orbit missions, SSH are usually referenced to an MSS in order to reduce possible geoid cross-track artifacts.

Three mean sea surface models have been selected for the GOCINA project. These three models have been released during 2000 and 2001 and are the newest mean sea surface models available. These are

|  | mean sea surfaces |
| --- | --- |
| Selected | CLS-01 (Centre de Localisation d’ Satellittes) – France KMS-01 (National survey and Cadastre) – Denmark GSFC-00 (Goddard Space Flight Center – Maryland, USA |
| Older surfaces. | OSU95 (Ohio State University, Columby, USA) CSR98 (University of Austin, Texas, USA). |

Table 1. Mean sea surface models.

All surfaces are computed and delivered on a 2' grid oceanwide between latitude ±80°(GSFC00) or  ±82° (CLS01 and KMS01). This resolution corresponds to 4 km at the Equator.

Section 2 below describes the individual mean sea surfaces. Section 3. presents the mean sea surfaces for the region of interest for the GOCINA project.

For evaluation and global comparison between the three mean sea surfaces the reader is referred to Hernandez and Schaeffer, (2000, 2001).

2. Mean sea surface Description.

Below a summay of the different data and processing applied to the individual mean sea surfaces.

| CLS 01 | T/P mean profile | ERS mean profile | GEOSAT mean profila | ERS-1 geodetic data |
| --- | --- | --- | --- | --- |
| Selected time period | 1993-1999 7 years (cycles 11-280) | 1993-1999 5 years 64 cycles | 1987-1988 2 years (cycles 1-44) | 1994-95 - ERS-1 phase E - ERS-1 phase G |
| Coverage | 66°S-66°N | 82°S-82°N | 72°S-72°N | 82°S-82°N |
| Groundtracks spacing | 320 km | ~80 km | 160 km | ~8 km |
| Remarks | used to reference other data | referenced to T/P data. | old dataset less accurate correction | fine spatial resolution. each track adjusted to T/P mean profile |

Table 2. Characteristics for the CLS01 Mean sea surface.

| KMS 01 | T/P mean profile | ERS mean profile | GEOSAT geodetic data | ERS-1 geodetic data |
| --- | --- | --- | --- | --- |
| Selected time period | 1993-1998 6 years (cycles 11-232) | 1993-1999 5 years 60 cycles | 1985-1986 1.5 years (cycles 1-44) | 1994-95 - ERS-1 phase E - ERS-1 phase G |
| Coverage | 66°S-66°N | 82°S-82°N | 72°S-72°N | 82°S-82°N |
| Groundtracks spacing | 320 km | ~80 km | ~6 km | ~8 km |
| Total of used points | used to reference other data | ERS-1 and ERS2 referenced to T/P data separately. DGM04 orbits | old dataset less accurate correction corrected sea surface heights used | 2 interlaced repeats. fine spatial resolution. xover corrected sea surface heights used. |

Table 3. Characteristics for the KMS01 Mean sea surface.

| GSFC 00 | T/P mean profile | ERS mean profile | GEOSAT mean profile | GEOSAT geodetic mission | ERS-1 geodetic data |
| --- | --- | --- | --- | --- | --- |
| Selected time period | 1993-1998 6 years (cycles 11-232) | 1993-1997 3 phases used 48 cycles | 1987-1988 1.9 years (cycles 1-42) | 1985-1986 1.5 years | 1994-95 - ERS-1 phase E - ERS-1 phase G |
| Coverage | 66°S-66°N | 82°S-82°N | 72°S-72°N | 72°S-72°N | 82°S-82°N |
| Groundtracks spacing | 320 km | ~80 km | 160 km | ~6 km | ~8 km |
| Remarks | Used to reference other data. | referenced to T/P data separately. DGM04 orbits | old dataset less accurate correction | old dataset less accurate correction. fine resolution un-uniform coverage along track gradients used. | 2 interlaced repeats. fine spatial resolution. along track gradients used. |

Table 4. Characteristics for the GSFC00 Mean sea surface.

All 3 mean sea surfaces are derived from different (but somewhat similar) subset of altimetry. The major difference is the fact that the CLS mean sea surface only uses finer scale geodetic mission altimetry from the ERS-1 satellite whereas both GSFC00 and KMS01 uses the older and Geosat geodetic mission altimetry.

Figure 1: Global map of the MSS CLS01 (units in m). On the continents, the EGM96 geoid height is used.

Figure 2: Global map of the MSS KMS01 (units in m).

3. Comparison with EGM96 geoid in the GOCINA study region

Figure 3. Differences between CLS01  MSS and EGM96 geoid (same colorbar as Fig 5)

Figure 4. Differences between KMS01  MSS and EGM96 geoid (same colorbar as Fig 5)

Figure 5. Differences between GSFC00  MSS and EGM96 geoid

A comparison for the GOCINA region between the MSS surfaces and EGM96 geoid model is given in the table below (all values are in meters).

|  | Mean | Standard Deviation | Minimum | Maximum |
| --- | --- | --- | --- | --- |
| KMS01-EGM96 | -0.36 | 0.28 | -1.53 | 1.40 |
| GSC00-EGM96 | -0.35 | 0.28 | -1.43 | 1.33 |
| CLS01-EGM96 | -0.31 | 0.28 | -1.38 | 1.86 |

Table 4. Mean difference, standard deviation, minimum and maximum of difference between the Mean sea surface models and the EGM96 geoid model

4. Comparison between Different Mean sea surfaces

Figure 6. Differences between KMS01 and CLS01 MSS (KMS minus CLS). Color scale same as figure 8.

Figure 7. Differences between KMS01 and GSFC00 MSS (KMS minus GSFC). Color scale same as figure 8.

Figure 8. Differences between GSFC00 and CLS01 MSS (GSFC minus CLS).

A comparison for the GOCINA region between the surfaces are given in the table below (all values are in meters).

|  | Mean | Standard Deviation | Minimum | Maximum |
| --- | --- | --- | --- | --- |
| KMS01-GSFC00 | -0.01 | 0.11 | -1.17 | 0.70 |
| GSC00-CLS01 | -0.05 | 0.14 | -2.29 | 1.41 |
| KMS01-CLS01 | -0.01 | 0.13 | -1.95 | 1.22 |

Table 5. Mean difference, standard deviation, minimum and maximum of difference between the Mean sea surface models

5. Data

Ascii grids of the mean sea surfaces used for this comparison is available at

ftp.kms.dk/GOCINA/MSS

6. References

Hernandez, F. and P. Schaeffer, 2000: Altimetric Mean Sea Surfaces and Gravity Anomaly maps inter-comparisons AVI-NT-011-5242-CLS, 48 pp. CLS Ramonville St Agne.

Hernandez, F. and P. Schaeffer, 2001: The CLS01 Mean Sea Surface: A validation with the GSFC00 surface In press, CLS Ramonville St Agne.