## Slide 1: Towards a true Swarm of Magnetic Satellites - Scientific use of measurements taken by navigational magnetometers onboard Low-Earth orbiting satellites
Nils Olsen
DTU Space – Technical University of Denmark / DK
Satellites for measuring Earth’s magnetic field
On magnetometer data calibration
Successful examples: Cryosat-2, GRACE, GRACE-FO* Less successful examples: GOCE, Aeolus
Some scientific applications
*GRACE-FO calibration done by GFZ Potsdam

## Slide 3: Why more satellites for exploring Earth’s magnetic field?
No high-precision magnetic field data are available in the gap between CHAMP and Swarm (Oct 2010 and Nov 2013)

## Slide 4: Why more satellites for exploring Earth’s magnetic field?
Ionospheric and magnetospheric electric current systems are oriented wrt Sun
Single satellites only measure at one specific local time (slowly drifting in time)
Simultaneous magnetic data from many satellites allows to detangle time-space structure of external sources
Swarm Alpha, 1 Aug 2018
Swarm Alpha, 1 - 11 Aug 2018

## Slide 5: Most satellites carry magnetometer for navigational purposes as part of their AOCS (Attitude and Orbit Control System) The data of these AOCS magnetometers have scientific value but data calibration is essential Towards a true swarm of satellites …

## Slide 6: Why more satellites for exploring Earth’s magnetic field?
No high-precision magnetic field data are available in the gap between CHAMP and Swarm (Oct 2010 and Nov 2013)
CryoSat-2 and GRACE help to fill this gap, for improved study of the dynamics of Earth’s core field

## Slide 7: Why more satellites for exploring Earth’s magnetic field?
No high-precision magnetic field data are available in the gap between CHAMP and Swarm (Oct 2010 and Nov 2013)
CryoSat-2 and GRACE help to fill this gap, for improved study of the dynamics of Earth’s core field
Swarm, GRACE-FO and CSES provide simultaneous data for improved time-space separation of external sources

## Slide 8: Local Time evolution of Swarm, CryoSat-2 and GRACE
Swarm A/C change in LT of 2.73 hrs/month all LT in 4.4 months
Swarm B change in LT of 2.61 hrs/month all LT in 4.6 months
CryoSat-2 change in LT of 1.51 hrs/month all LT in 8.0 months
GRACE A/B change in LT of 2.24 hrs/month all LT in 5.3 months

## Slide 9: Local Time evolution of Swarm, CryoSat-2, GRACE-FO and CSES
Swarm A/C change in LT of 2.73 hrs/month all LT in 4.4 months
Swarm B change in LT of 2.61 hrs/month all LT in 4.6 months
CryoSat-2 change in LT of 1.50 hrs/month all LT in 8.0 months
GRACE-FO A/B change in LT of 0.59 hrs/month all LT in 20.2 months
CSES fixed LT at 02/14

## Slide 10: Cryosat-2
Launched in April 2010 – and still in operation
720 – 730 km altitude, 92° orbital inclination
3 platform vector Fluxgate magnetometers (FGMs), 4 sec sampling
3 Star imagers (STRs)
House-Keeping (HK) data available: magnetorquer currents, magnetometer temperature, …

## Slide 11: GRACE Satellite Duo
GRACE-A and GRACE-B follow each other with 220 km alongtrack distance
Between March 2002 and October 2017, 92° orbital inclination

## Slide 12: GRACE Satellite Duo
GRACE-A and GRACE-B follow each other with 220 km alongtrack distance
March 2002 and October 2017, 92° orbital inclination
1 Fluxgate magnetometer (FGM) on short boom, 1 sec sampling (since 2008), 26 nT digitisation steps
2 Star imagers (STRs) on satellite body
HK data: magnetorquer currents, battery and solar array currents, but no magnetometer temperature

## Slide 13: Terminology …
Calibration: From Vector Fluxgate Magnetometer (FGM) 3-sensor output E to magnetic field BFGM vector in FGM frame Estimation of the parameters describing FGM calibration and applying them to sensor output E in order to get BFGM in physical units (nT) in an orthogonalized instrument frame
Alignment: Rotation of BFGM from FGM frame to Star Imager (STR) frame and further to BNEC in NEC (North-East-Center) frame Estimation of rotation parameters (“Euler angles”) and applying them to BFGM using STR attitude data q in order to get magnetic field vector BNEC in NEC frame
Correction for disturbance magnetic field DB: Accounting for influence from instrument and S/C e.g. magnetorquer disturbance field Estimation of disturbance parameters and correction of BFGM Often done by co-estimation with calibration parameters

## Slide 14: Calibration and Alignment of a Vector Magnetometer
E is uncalibrated output of the 3 sensors, BFGM is calibrated magnetic field vector in FGM frame
Assumption: linear response of each FGM instrument: 3 offsets (biases), 3 scale values (sensitivities), 3 non-orthogonalities
Alignment: rotation from FGM to STR (Common Reference Frame of Star tracker)
3 Euler angles for describing rotation matrix 12 parameters
From STR to NEC frame with attitude information (STR quaternions q)

## Slide 15: Scalar Calibration vs Vector Calibration
Scalar Calibration Estimation of 9 FGM parameters by minimizing < DF2 = (|BFGM| - |Bmod|)2 > or < DF2 = (|BFGM| - Fabs)2 > (provided availability of absolute scalar measurements Fabs)
  Preferred solution for satellites that carry an absolute scalar instrument (Ørsted, CHAMP, Swarm)
  Magnetic field intensity F is less influenced by magnetic signature of ionospheric field-algned currents, thus data from polar latitudes can be included in calibration process
  Usually much smaller rms misfit (factor 3 -5) than vector calibration Better estimation of F compared to vector calibration
  Less sensitive to calibration parameters: some parameters are poorly resolved, and Euler angles are completely unresolved
Vector Calibration Estimation of 9 FGM parameters and 3 Euler angles (= 12 paremeters) by minimizing of < DB2 = |BFGM – Bmod|2 >
  Preferred solution provided good model vector field Bmod is available and stable mounting of FGM and STR
  Less suitable for boom-mounted FGM mounted and satellite-mounted STR due to boom bending DF2 = (|BFGM| - |Bmod|)2
Good model values Bmod or Fmod = |Bmod| are required to calibrate magnetometer on satellites without absolute scalar magnetometer
For that we use CHAOS-7 model predictions (core, crust, magnetosphere + induced) calculated for the time and position of each data point

## Slide 16: Scalar Calibration vs Vector Calibration
Scalar Calibration Estimation of 9 FGM parameters by minimizing < DF2 = (|BFGM| - |Bmod|)2 > or < DF2 = (|BFGM| - Fabs)2 > (provided availability of absolute scalar measurements Fabs)
  Preferred solution for satellites that carry an absolute scalar instrument (Ørsted, CHAMP, Swarm)
  Magnetic field intensity F is less influenced by magnetic signature of ionospheric field-algned currents, thus data from polar latitudes can be included in calibration process
  Usually much smaller rms misfit (factor 3 -5) than vector calibration Better estimation of F compared to vector calibration
  Less sensitive to calibration parameters: some parameters are poorly resolved, and Euler angles are completely unresolved
Vector Calibration Estimation of 9 FGM parameters and 3 Euler angles (= 12 paremeters) by minimizing of < DB2 = |BFGM – Bmod|2 >
  Preferred solution provided good model vector field Bmod is available and stable mounting of FGM and STR
  Less suitable for boom-mounted FGM mounted and satellite-mounted STR due to boom bending
CryoSat-2: vector calibration (possible because of body-mounted FGM and STR)
GRACE: combined scalar and vector calibration (vector calibration alone would result in larger scatter of FGM calibration parameters due to boom bending)

## Slide 17: CryoSat-2: Accounting for temperature, s/c disturbance, and non-linearities
12 “basic” calibration parameters, estimated separately for each of the 100 months (Aug 2010 – Dec 2018) x 12 = 1200 parameters
The 3 offsets b and 3 scale values S depend on sensor temperature TFGM Assumed to be constant for whole mission: 2 x 3 = 6 parameters
Magnetic disturbance vector of Magnetorquer currents IMTQ Assumed to be constant for whole mission: 3 x 3 tensor = 9 parameters
Magnetic disturbances due to solar array and battery current strengths ISA1, ISA2, IBatt Assumed to be constant for whole mission: 3 x 3 = 9 parameters
Non-linearities (“transverse effect” disturbance of fluxgate sensor x on sensor output y) B1 depends on E32, and B3 depends on E23 and E32 : 3 parameters
In total 1227 model parameters estimated by robust non-linear Least-Squares from 13.3 mio observations (= 3 x 4.4 mio data triplets)
Temporal regularisation (smoothing) of month-to-month variation of “basic” 12 parameters
Vector calibration, minimizing average of DB2 = |BFGM – Bmod|2

## Slide 18: Magnetic field strength F = |B| August 2018
observed Fobs
model Fmod
CryoSat-2
Swarm A
430 km altitude
720 km altitude

## Slide 19: Magnetic field strength F = |B| August 2018
Swarm A
DF = Fobs – Fmod
CryoSat-2, uncalibrated
Polar ionospheric currents

## Slide 20: Magnetic field strength F = |B| August 2018
CryoSat-2, calibrated
Swarm A
DF = Fobs – Fmod
Polar ionospheric currents
weaker in CryoSat, due to higher altitude

## Slide 21: Magnetic field strength F = |B| August 2018
CryoSat-2, calibrated
Swarm A
DF = Fobs – Fmod
dayside
nightside
1.9 nT rms measurement error: < 0.5 nT
6 nT rms
1 min (15 values) moving average

## Slide 22: CryoSat-2: Temporal Evolution of Calibration and Alignment Parameters
For FGM1
Month-to-month variation:
Offsets: ± 8 nT
Scale values: ± 300 ppm
non-orthononalities and Euler angles: ±0.02° (±72 arcsecs)

## Slide 23: CryoSat-2: Daily rms misfit of 5 – 10 nT

## Slide 24: GRACE: How to account for magnetometer temperature effects?
GRACE magnetometer temperature data are not available (not part of HK data)
Fluxgate magnetometer output depend on sensor temperature
  up to 30 ppm/°C for Swarm scale values,
  up to 100 ppm/°C for CryoSat-2 scale values, measured DT of ±6 °C results in ±600 ppm change, corresponding to ±30 nT @ 50 000 nT
Proxy for magnetometer temperature: Sun position angles a,b wrt spacecraft (same approach as used for correcting dBSun disturbance on Swarm satellites)
Dependency of FGM offsets and scale values, and of Euler angles (boom bending!) on Sun position

## Slide 25: GRACE: Calibration model parameterization
12 “basic” calibration parameters, estimated separately for each of the 118 months (Jan 2008 – Oct 2017) x 12 = 1416 parameters
The 3 offsets b, 3 scale values S, and 3 Euler angles depend on Sun position angle a,b Spherical harmonic expansion, assumed to be constant for whole mission: 342 parameters
Magnetic disturbance vector of Magnetorquer currents IMTQ Assumed to be constant for whole mission: 3 x 3 tensor = 9 parameters
Magnetic disturbances due to solar array and battery current strengths ISA1, ISA2, IBatt Assumed to be constant for whole mission: 3 x 3 = 9 parameters
Non-linearities (“transverse effect” disturbance of fluxgate sensor x on sensor output y): 48 parameters
In total 1839 model parameters estimated by robust non-linear Least-Squares from 10.5 mio observations (= 3 x 2.62 mio vector triplets + 2.62 scalar values) for each satellite
Temporal regularisation (smoothing) of month-to-month variation of “basic” 12 parameters
Combined scalar and vector calibration, minimizing weighted average of 5<DF2> + <|DB|2> = 5< (|BFGM| - |Bmod|)2 > + < |BFGM – Bmod|2 > scalar residuals are upweighted by factor 5

## Slide 26: GRACE: Temporal Evolution of Calibration and Alignment Parameters
For GRACE-A
Month-to-month variation:
Offsets: ± 10 nT
Scale values: ± 200 ppm
non-orthononalities and Euler angles: ±0.01° (±36 arcsecs)

## Slide 27: GRACE-A: DB = Bobs – BCHAOS-7 for 10 to 19 August 2010
FACs in horizontal components BN, BE in auroral regions
Polar Electrojets in vertical component BC and scalar field F in auroral regions

## Slide 28: Less successful calibrations: GOCE and Aeolus
March 2009 – November 2013
255 km altitude, lowered to 235 km in November 2012
3 platform vector Fluxgate magnetometers (FGMs), 16 sec sampling
2 Star imagers (STRs)
House-Keeping (HK) data available: magnetorquer currents, magnetometer temperature, …

## Slide 29: Less successful calibrations: GOCE and Aeolus
March 2009 – November 2013
255 km altitude, lowered to 235 km in November 2012
3 platform vector Fluxgate magnetometers (FGMs), 16 sec sampling
2 Star imagers (STRs)
House-Keeping (HK) data available: magnetorquer currents, magnetometer temperature, …
Large scatter in all components and scalar field F, no clear geophysical signal visible

## Slide 30: Less successful calibrations: GOCE and Aeolus
Daily rms: 10 nT at best, increased to > 30 nT during (northern) summer (?)
Orbit-to-orbit variation of calibration parameters (see next talk by Rekowski et al)
Note: GOCE magnetic data can still be used for determination of e.g. FACs in polar regions after high-pass filtering on orbit-by-orbit basis. However, the coarse 16 sec sampling rate make GOCE data less interesting for external field investigations

## Slide 31: Less successful calibrations: GOCE and Aeolus
Launched in August 2018
320 km altitude
1 platform vector AMR (Anisotropic Magneto Resistive) magnetometer, 10 sec sampling
14 – 21 Oct 2018, 26 nT rms in DF

## Slide 32: Application: Monitoring of Magnetospheric Ring-current activity
Independent observation of time-evolution of magnetospheric ring-current with magnetic data from 6 satellites …
… and comparison with Dst-index derived from ground magnetic data

## Slide 33: Space-time structure of magnetospheric field
Joint spherical harmonic analysis using magnetic data from 6 satellites
q10 is main ring-current term
describes symmetric ring-current in equatorial plane
Terms describing asymmetric ring-current
Strong asymmetric ring current during storm expansion phase contributions from terms with m = 1, faster decay compared to main term

## Slide 34: Application: Monitoring of Magnetospheric Ring-current activity
Independent observation of time-evolution of magnetospheric ring-current with magnetic data from 5 satellites …
… and comparison with Dst-index derived from ground magnetic data
50 nT
Dst
CSES
GRACE-FO
CryoSat-2
Swarm B
Swarm A

## Slide 35: Space-time structure of magnetospheric field
Joint spherical harmonic analysis using magnetic data from 5 satellites
q10 is main ring-current term
describes symmetric ring-current in equatorial plane
Terms describing asymmetric ring-current
Strong asymmetric ring current during storm expansion phase contributions from terms with m = 1, faster decay compared to main term

## Slide 36: Application: Core surface field secular acceleration
CHAOS-7 model of Earth’s magnetic field up to spherical harmonic degree n = 19
in 2015 at surface of Earth’s core (r = 3485 km)

## Slide 37: Application: Core surface field secular acceleration
Only ground observatories
Swarm
CHAMP
CHAOS-7

## Slide 38: Application: Core surface field secular acceleration
SOLA: Local Inversion of CHAMP, Cryosat and Swarm data (Hammer & Finlay 2019)
Swarm
CHAMP
Cryosat
CHAOS-7

## Slide 39: Summary and Conclusion
Almost every satellite carries magnetometers for navigational purposes Their data can be used for scientific investigations – after calibration
Quality of magnetometer data and s/c disturbances is very different from satellite to satellite – be prepared for surprises!
Data can be used for core field studies and for investigating ionospheric and magnetospheric current systems - Space-weather applications
Enormous potential for science and application
Magnetic data for CryoSat-2 (GRACE and GRACE-FO will follow soon) are available as daily files in CDF (similar to Swarm L1b data) at ftp://swarm-diss.eo.esa.int/ and at Swarm ViRES/VRE online service https://vires.services
We are working towards calibration and distribution of platform magnetometer data from other ESA satellite missions (e.g. Sentinel-3, …)